## Slide 1
Roadmap for today (adding in renewables)
How we make electricity from burning fossil fuels (or renewables or nuclear)
How we refine the oil we extract from the ground (for burning, and also to make plastics)
Forms of fossil fuels (coal, oil, gas)
Forms of renewable fuels: carbohydrates, sugars, alcohols)
How we extract fossil fuels from the ground
What burning has to do with chemical bonds

## Slide 2
  Hydrocarbon
  Alcohol
  Sugar
  Acid
  Ester
Categories of organic compounds (some are fuels, some just smell nice)

## Slide 3
We can ferment sugars, carbohydrates, and cellulosic (leafy) parts

## Slide 4
We can ferment sugars, carbohydrates, and cellulosic (leafy) parts

## Slide 5
Roadmap for today (adding in renewables)
How we make electricity from burning fossil fuels (or anything else)
How we refine the oil we extract from the ground (for burning, and also to make plastics)
Forms of fossil fuels (coal, oil, gas)
Forms of renewable fuels: carbohydrates, sugars, alcohols)
How we extract fossil fuels from the ground
What burning has to do with chemical bonds

## Slide 6: Fuel = something that burns
Usually CO2 and H2O
(But there can be other products too … including heat!)
Usually O2
(But can be other oxidizers too)
Glucose: C6H12O6
Coal: C(s)
Oil/gas: CnHm(l or g)
What burning has to do with chemical bonds

## Slide 7: Net heat released is due to the difference in bond strength
Energy
2H2O + CO2
Net heat released =
CH4 + 2O2
Bonds breaking
Bonds forming
As long as the bonds forming are stronger than the bonds that are breaking, heat is released!
This is often the case because O=O is pretty weak for a double bond (only 500 kJ/mol), whereas C=O is pretty strong for a double bond (800 kJ/mol)
What burning has to do with chemical bonds

## Slide 8: How do we know those numbers?
Bomb calorimeter
(lab)
What burning has to do with chemical bonds

## Slide 9: Measuring vs getting info from labels
Summary of bomb calorimetry equations
The heat released depends on how much the temperature went up:
where is based on how much water there is in the calorimeter. Then the specific enthalpy of combustion is
where is the mass of the sample you put in the cup (before you burn it!!!)
Summary of
nutrition equations
1 Calorie = 1 kcal = 1000 calories
1 kcal = 4.18 kJ
The specific enthalpy of combustion (or digestion) is the energy per serving divided by the grams per serving.
Your task … what’s the fuel with the highest specific enthalpy of combustion (also called energy density): wood pellets, cooking oil, or option #3? How do they compare with fossil fuels?
What burning has to do with chemical bonds

## Slide 10
Energy density per gram
What burning has to do with chemical bonds
Wood pellets, cookies
Olive oil
Alcohol (ethanol)

## Slide 11
Converting energy density per gram to per mole of fuel
Can you use this to find for ethanol on a per mole basis?
One mole of ethanol weighs 46 grams ()
What burning has to do with chemical bonds

## Slide 12
Converting energy density per gram to per mole of fuel
Can you use this to find for ethanol on a per mole basis?
One mole of ethanol weighs 46 grams ()
What burning has to do with chemical bonds

## Slide 13
Converting energy density per gram to per mole of fuel
Can you use this to find for methane on a per mole basis?
One mole of methane weighs … grams ()
…
What burning has to do with chemical bonds

## Slide 14
Converting energy density per gram to per mole of fuel
Can you use this to find for methane on a per mole basis?
One mole of methane weighs … grams ()
What burning has to do with chemical bonds

## Slide 15
Roadmap for today (adding in renewables)
How we make electricity from burning fossil fuels (or renewables or nuclear)
How we refine the oil we extract from the ground (for burning, and also to make plastics)
Forms of fossil fuels (coal, oil, gas)
Forms of renewable fuels: carbohydrates, sugars, alcohols)
How we extract fossil fuels from the ground
What burning has to do with chemical bonds

## Slide 16
Burning coal/oil/gas or burning biofuel
or collecting solar
Nuclear fission
Solar energy
How we make electricity from burning fossil fuels (or renewables or nuclear)

## Slide 17
Roadmap for today (adding in renewables)
How we make electricity from burning fossil fuels (or renewables or nuclear)
How we refine the oil we extract from the ground (for burning, and also to make plastics)
Forms of fossil fuels (coal, oil, gas)
Forms of renewable fuels: carbohydrates, sugars, alcohols)
How we extract fossil fuels from the ground
What burning has to do with chemical bonds

## Slide 18
Switchgrass
Sugarcane
Corn
Fruit
Ethics of biofuels: many are also food, or replace food crops